## Slide 1
A CPI PROJECT ON NETWORK SECURITY
Network Traffic Analysis
& Hybrid Intrusion Detection
Turning Raw Network Traffic into Actionable Security Insights
♦ ♦ ♦
CPI — Creativity, Problem Solving and Innovation
OBJECTIVES PHASE
Notes: Good morning. Our project for CPI is called Network Traffic Analysis and Hybrid Intrusion Detection. An Intrusion Detection System, or IDS, is simply a tool that watches network traffic and raises an alert when something looks like an attack. I want to be clear right at the start that we are in the Objectives phase of the subject, so I am not presenting a finished product today. What I will cover is the problem we identified, the direction we are proposing to solve it, and most importantly the three specific objectives we plan to reach and the exact number we will use to check each one.

## Slide 2
I. THE PROBLEM
Finding the Threat Hidden in the Traffic
♦ Modern networks generate enormous volumes of traffic.
♦ Attacks hide inside ordinary, legitimate activity.
♦ Manual packet inspection is slow and error-prone.
♦ No analyst can realistically read millions of packets.
THE CORE DIFFICULTY
Finding malicious packets by hand is like looking for a few suspicious letters inside an entire city's mail.
The volume is the problem — not any single packet.
MILLIONS OF PACKETS
Normal traffic, generated every second
A FEW SUSPICIOUS
Scanning, flooding, spoofing, exfiltration
ONE ANALYST
Limited time and attention
Notes: Every device on a network constantly sends and receives small chunks of data called packets. Even on a small network that adds up to millions of packets very quickly. The difficulty is that an attack — for example, someone scanning our machine to see which doors are open — is only a handful of packets sitting inside all of that normal traffic. A human analyst cannot open a packet capture file, that is a PCAP or Packet Capture, and read through millions of rows one by one. So important warning signs are either missed or noticed far too late. The analogy we like is this: doing it by hand is like searching for a few suspicious letters inside an entire city's mail. The individual letter is not hard to understand — finding it is.

## Slide 3
II. THE PROPOSED SOLUTION
From Raw Traffic to Actionable Alerts
We propose a lightweight pipeline that converts large volumes of raw network traffic into a much smaller set of contextualised, reviewable events.
I
Network Traffic
/ PCAP
II
Packet
Parsing
III
Threat
Detection
IV
MITRE ATT&CK
Mapping
V
Threat Intel
Enrichment
VI
Interactive
Dashboard
VII
Human
Review
The goal is not to replace the analyst — it is to reduce the volume of data the analyst has to investigate manually.
PLANNED TECHNOLOGY STACK
Python · Scapy · DuckDB · Streamlit · MITRE ATT&CK · AbuseIPDB · VirusTotal · MaxMind GeoLite2
Notes: This is the direction we are proposing. Traffic comes in either as a saved PCAP file or as live capture. A parser pulls out the useful header fields — who sent the packet, to whom, which protocol, how big it was. Then a detection stage checks those records against rules. Anything flagged gets mapped to MITRE ATT&CK — that stands for MITRE Adversarial Tactics, Techniques and Common Knowledge, which is the industry-standard catalogue of attacker behaviours — and then enriched with outside information about the IP address, IP meaning Internet Protocol. Everything is finally shown on a dashboard. Notice the last box: a human still makes the decision. That is deliberate. We are not trying to replace the analyst, only to shrink what they have to look through.

## Slide 4
III. OBJECTIVE I
Build the Detection Pipeline
We aim to design a functional pipeline that converts raw PCAP or live network traffic into structured records and automatically identifies common suspicious network behaviour.
PLANNED DETECTION CATEGORIES
♦ Port Scanning
♦ SYN Flooding
♦ ARP Spoofing
♦ DNS Tunneling
♦ ICMP Flooding
♦ Malformed TCP Flags
Six rule-based signatures, each targeting a well-documented network behaviour.
≥ 90%
TARGET ATTACK DETECTION RATE
of simulated attacks detected across the six categories in controlled test captures.
HOW WILL WE MEASURE IT?
Run known, synthetically generated attack traffic through the system, then compare the attacks we injected against the detections the engine produces.
Notes: Our first objective is the detection pipeline itself. We aim to take raw traffic and automatically identify six well-known suspicious behaviours. Port scanning is someone knocking on many doors to see which are open. SYN flooding — SYN is the first message of a TCP, Transmission Control Protocol, connection — means opening thousands of half-finished connections to exhaust a server. ARP spoofing, ARP being Address Resolution Protocol, is a device lying about its identity on the local network. DNS tunneling, DNS meaning Domain Name System, hides data inside ordinary-looking name lookups. ICMP flooding, ICMP being Internet Control Message Protocol, is ping traffic used to overwhelm a target. And malformed flag combinations are packets deliberately built in invalid ways to slip past filters. The target we are committing to is at least ninety percent detection, and we can measure it honestly because we generate the attacks ourselves and know exactly what should have been caught.

## Slide 5
IV. OBJECTIVE II
Turning Alerts into Context
"What happened, what technique does it resemble, and how suspicious is the source?"
♦ Map every detection to a MITRE ATT&CK technique ID.
♦ Enrich flagged external IPs with reputation data.
♦ Add GeoIP country and city context.
♦ Offer optional, on-demand VirusTotal lookups.
100%
MITRE ATT&CK MAPPING
Every detection carries a technique ID.
≥ 95%
INTELLIGENCE ENRICHMENT
Reputation and location on flagged IPs.
THE TRANSFORMATION
RAW ALERT
"Suspicious IP detected"
CONTEXTUALISED ALERT
♦ Attack type
♦ MITRE ATT&CK technique ID
♦ IP reputation score
♦ Geographic location
♦ Threat intelligence detail
Notes: The second objective is about context. Simply detecting something is not enough — an alert that only says 'suspicious IP detected' does not help anyone decide what to do next. So for every detection we want to attach three things: a MITRE ATT&CK technique ID, so the alert has a standard name that any security team would recognise; a reputation score, which tells us whether that address has already been reported for abuse by other people; and a rough geographic location. For anything that needs a closer look, we plan an on-demand VirusTotal check rather than querying every address automatically, because the free API limits are small. Our targets here are deliberately strict and easy to audit — every single detection mapped, and at least ninety-five percent of flagged external addresses enriched.

## Slide 6
V. OBJECTIVE III
Making Investigation Simple
Network Traffic Analysis — Dashboard
PACKETS PARSED
DETECTIONS
FLAGGED IPs
TIME
SOURCE IP
DETECTION
MITRE ID
REPUTATION
CONCEPTUAL LAYOUT — NOT A FINAL SCREENSHOT
PLANNED FUNCTIONALITY
♦ View and filter detected events
♦ Sort and drill into individual alerts
♦ See MITRE ATT&CK detail inline
♦ See reputation and location context
< 3 sec
DASHBOARD LOAD TIME
100,000+
PACKETS TESTED
The dashboard should load and render a dataset of this size within the target time.
Notes: The third objective is usability. All of this data is useless if you need to write database queries to read it. We aim to build a dashboard using Streamlit, which is a Python library for building simple web interfaces, sitting on top of DuckDB, a lightweight database that is very fast at aggregating large tables. The user should be able to see the detected events, filter and sort them, and click into a single alert to see its full context — without touching raw packet data or writing SQL. What you see on the left is only a conceptual layout to show the idea, not a screenshot, because implementation belongs to a later phase. Our measurable target is that results from a dataset of a hundred thousand packets load in under three seconds.

## Slide 7
VI. OBJECTIVES AT A GLANCE
How Will We Know the Project Works?
OBJECTIVE
INTENDED OUTCOME
SUCCESS METRIC
Detection
Identify common network attacks
≥ 90% simulated attack detection
Context
Explain and enrich every alert
100% mapping · ≥ 95% enrichment
Investigation
Make results easy to analyse
100,000+ packets shown in < 3 sec
Each objective is independently testable and measurable.
DETECT
UNDERSTAND
INVESTIGATE
Notes: This slide is really the answer to the question a professor would ask: how will you know whether you succeeded? Each of our three objectives has exactly one number attached to it, and each can be tested on its own. Detection is tested by running attack traffic we generated ourselves and counting what the engine caught. Context is tested by auditing what fraction of the alerts came out with complete information attached. Investigation is tested by simply timing the dashboard against a fixed dataset of a hundred thousand packets. The whole story of the project fits into three words at the bottom: detect, understand, investigate.

## Slide 8
VII. PROJECT DIRECTION
What These Objectives Lead To
Achieving these three objectives gives us the foundation of a lightweight network intrusion detection and analysis system — suited to cybersecurity learning, small lab networks and proof-of-concept security monitoring.
RAW TRAFFIC
Packets captured or imported
DETECT
Six rule-based signatures
CONTEXTUALIZE
Framework mapping and intelligence
REVIEW
Confirmed threat or false positive
FUTURE EXTENSION — NOT A CURRENT CORE OBJECTIVE
Anomaly-based detection using an Isolation Forest model could later flag statistically unusual traffic that fixed rules were never designed to recognise. This remains optional and sits outside the three objectives defined for this phase.
♦ ♦ ♦
The aim is to transform overwhelming network traffic into a small set of understandable, actionable security events.
Notes: To wrap up: if we achieve these three objectives, what we end up with is a small, explainable intrusion detection and analysis system. It is useful for learning, for monitoring a small lab network, and as a proof of concept for the kind of pipeline that a Security Operations Center, or SOC, runs at a far larger scale. We have also noted one possible future extension — an Isolation Forest, which is a machine learning method that flags unusual data points without needing labelled examples of attacks. I want to stress that this is optional and is not one of our three objectives for this phase; we mention it only to show where the project could grow. For now our aim is exactly the sentence at the bottom: turn overwhelming network traffic into a small set of understandable, actionable security events. Thank you — happy to take questions.